## Slide 1: FILL IN WITH TEXT
Steering Horizon Controller CORE/CDX746/7 UPV0 status updated
02/22/2021
Richard Li – Feature Owner
Brian Atherton – Feature Owner
Lisa Waszczenko - Supervisor

## Slide 2
Concept - Steering Horizon Controller
Current Strategy
Tilt / Tele
A
B
C
D
A
C
B
D
A
B C D
New Strategy
Current Strategy
E
Summary of the Change |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Definition of the Change/Problem: | The Driver needs to reach multiple switches from different locations to perform cruise control, adjust/fold rear mirrors, adjust steering column and pedals. CIED desires a programmable switch interface on the steering wheel to maintain line of sight on the high heads up display. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Description of the Proposed Changes: | Combined Cruise Control with Mirror adjust & fold, steering column control and adjustable pedal on the steering Horizon Controller AND show on DISPLAY. Utilized Phoenix domain controller to translate switch inputs to menu/icon on display and perform switch input logic to determine CAN signals to features actuators. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Justification why the proposed changes should be implemented: | protecting eyes up and out – ALL Control content consistently show on display Reducing operating complexity – Combining four around switches to current steering wheel switches. Reducing hardware and JITs cost - eliminating ACC, Mirror, Column and Pedal four sets Switches Increasing interior Enjoyable experience – Streamlined design More Capacity – Through add menu /ICON to control more features |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
  Proposal
  Using configurable switch interface to Combine Cruise Control (A) with Mirror ADJUST & MIRROR FOLD (B), steering column control (C) AND ADJUSTABLE PEDAL(D) on the steering Horizon Controller AND show on DISPLAY (E).
  Benefits
protecting eyes up and out – ALL Control content consistently show on display
Reducing operating complexity – Combining Seven around switches to current steering wheel switches.
Reducing hardware and JITs cost - eliminating ACC, Mirror, Column and Pedal five sets Switches
Increasing interior Enjoyable experience – Streamlined design
More Capacity – Through add menu /ICON to control more features

## Slide 3
Power Adjustable Mirrors and Fold Mirrors (w/ Autofold)
Pedal Actuator
PC Actuator
Mirror Actuator
Customer Output
CC Actuator
Power Pedal (Tilt) network Diagram
SIMA
Switch input Module A
Private
CAN
FD3-CAN
Cruise Control Network Diagram
Power Column (tilt/tele) Network Diagram
Improved Steering Horizon Controller Boundary Diagram
SCCM
Steer Column Control Module
ECG2
Enhance central Gateway
Phoenix Domain Controller
DSM
Driver seat control module
FD3-CAN
BCM
Body Control Module
HS1-CAN
DDM
Driver Door Control Module
Lpos_1
Lpos_2
Lpos_3
Lpos_4
Lpos_5
Lpos_6
Lpos_7
Lpos_8
Lpos_9
Lprespos_1
Lprespos_2
Lprespos_3
Lprespos_4
Lprespos_5
Lprespos_6
Lprespos_7
Lprespos_8
Lprespos_9
Rpos_1
Rpos_2
Rpos_3
Rpos_4
Rpos_5
Rpos_6
Rpos_7
Rpos_8
Rpos_9
Rprespos_1
Rprespos_2
Rprespos_3
Rprespos_4
Rprespos_5
Rprespos_6
Rprespos_7
Rprespos_8
Rprespos_9
Menu
Menu
Menu up
Menu down
OK
RADIO/PPT
PPT
Vol +
Vol -
Seek left
Seek right
Phone
Phone - Accept
Phone - Reject
Vol +
Vol -
St Column
Tilt +
Tilt -
Tele +
Tele -
Mirror LH
Tilt +
Tilt -
Tele +
Tele -
Mirror RH
Tilt +
Tilt -
Tele +
Tele -
HS2-CAN
DAT-ACC
on
off
Can
Lateral Control
Res +
Set -
Gap
HS3-CAN
Switch status signals
Feature actuation signals
PCM
FD3-CAN
DDM
Driver Door Control Module
FD3-CAN
DSM
Driver seat control module
DDM
Driver Door Control Module
Summary
Utilized Phoenix domain controller to to translate 18 switch signal logic combination to more 60 CAN signals.
No need new ECU module.
Customer Input – Switch button push

## Slide 4
Power Adjustable Mirrors and Fold Mirrors (w/ Autofold)
Mirror Actuator
Customer
Private
CAN
FD3-CAN
How Horizon Controller Works?
SCCM
ECG2
Phoenix Domain Controller
BCM
HS1-CAN
DDM
Lpos_1
Lpos_2
Lpos_3
Lpos_4
Lpos_5
Lpos_6
Lpos_7
Lpos_8
Lpos_9
Lprespos_1
Lprespos_2
Lprespos_3
Lprespos_4
Lprespos_5
Lprespos_6
Lprespos_7
Lprespos_8
Lprespos_9
Rpos_1
Rpos_2
Rpos_3
Rpos_4
Rpos_5
Rpos_6
Rpos_7
Rpos_8
Rpos_9
Rprespos_1
Rprespos_2
Rprespos_3
Rprespos_4
Rprespos_5
Rprespos_6
Rprespos_7
Rprespos_8
Rprespos_9
Menu
Menu
Menu up
Menu down
OK
RADIO/PPT
PPT
Vol +
Vol -
Seek left
Seek right
Phone
Phone - Accept
Phone - Reject
Vol +
Vol -
St Column
Tilt +
Tilt -
Tele +
Tele -
Mirror LH
Tilt +
Tilt -
Tele +
Tele -
Mirror RH
Tilt +
Tilt -
Tele +
Tele -
HS3-CAN
HS2-CAN
1
2
3
4
1
2
3
4
5
5
= Logic Ops(1,2,3,4) = (RH Mirror Tilt -)
Switch status signals
Feature actuation signals
DAT-ACC
on
off
Can
Lateral Control
Res +
Set -
Gap
Touch anywhere on switch to wake up screen
SIMA

## Slide 5
Customer
SIMA
Switch input Module A
Private
CAN
FD3-CAN
Steering Horizon Controller Major Change Point Analysis
SCCM
Steer Column Control Module
ECG2
Enhance central Gateway
Phoenix Domain Controller
FD3-CAN
HS1-CAN
Lpos_1
Lpos_2
Lpos_3
Lpos_4
Lpos_5
Lpos_6
Lpos_7
Lpos_8
Lpos_9
Lprespos_1
Lprespos_2
Lprespos_3
Lprespos_4
Lprespos_5
Lprespos_6
Lprespos_7
Lprespos_8
Lprespos_9
Rpos_1
Rpos_2
Rpos_3
Rpos_4
Rpos_5
Rpos_6
Rpos_7
Rpos_8
Rpos_9
Rprespos_1
Rprespos_2
Rprespos_3
Rprespos_4
Rprespos_5
Rprespos_6
Rprespos_7
Rprespos_8
Rprespos_9
Menu
Menu
Menu up
Menu down
OK
RADIO/PPT
PPT
Vol +
Vol -
Seek left
Seek right
Phone
Phone - Accept
Phone - Reject
Vol +
Vol -
St Column
Tilt +
Tilt -
Tele +
Tele -
Mirror LH
Tilt +
Tilt -
Tele +
Tele -
Mirror RH
Tilt +
Tilt -
Tele +
Tele -
HS2-CAN
DAT-ACC
on
off
Can
Lateral
Res +
Set -
Gap
HS3-CAN
Switch status signals
Feature actuation signals
FD3-CAN
FD3-CAN
Power Adjustable Mirrors and Fold Mirrors (w/ Autofold)
Pedal Actuator
PC Actuator
Mirror Actuator
CC Actuator
Power Pedal (Tilt) network Diagram
Cruise Control Network Diagram
Power Column (tilt/tele) Network Diagram
DSM
Driver seat control module
BCM
Body Control Module
DDM
Driver Door Control Module
PCM
DDM
Driver Door Control Module
DSM
Driver seat control module
DDM
Driver Door Control Module
Summary
Utilized Phoenix domain controller to translate switch inputs to menu and icon on display and perform switch input logic to determine CAN signals to features actuators.
No need new module.
1. Switch – J. Murphy, R. Kern, S Magiera
1.1. New design w/new signals – From 7 sets of switches to 2 sets of switches.
1.2. Multi function switch.
1.3. Increase durability cycles.
1.4. Worst case study – Abuse loading
Carryover
2. Need carryover each feature input signals from GWM as ECG2 output signals
3. STSS IVI – G. Cheng, R. Paquette
ECG2 & Phoenix Domain Controller spec
4. Display Cluster – J. Gregoire, J. Asirvatham
Handle menu & ICON on display based on switch input.
5. Phoenix Domain Control –
Logic coding based on switch signals to actuator signals.
6. IVIC, BD - Hamid Mahmood, Joey Oravec
7. EESE Physical Architecture -
8. Software – Anita Stoffer
7. EESE Physical Architecture – Z Deljevic , Bruce Williams
9. MBSE – Jorge Napoles

## Slide 6
Issue Title: | 2024 CDX74X Steering Horizon Controller |  |  | Champion: Team Leader: |  | Sonya Bentley Lisa Waszczenko |  |  | 
Source: |  |  |  | Team: |  | Richard Li, Brian Atherton, Vikram Gokhale |  |  | 
Issue Description: | Unable to meet UPV0 timing for CDX746/7 Steering Horizon Controller features |  |  |  |  |  |  |  | 
Containment: | 1- Weekly meetings with FMA team to review updates and complete FMA Documents. 2- Weekly meetings with carryover FOs and Functional Architecture to engineer the interactions between features and ECGs. 3- Weekly meetings with Phoenix, display, Architecture and software teams to manage interface and interactions between features. 4- Weekly meetings with MBSE modeler to finish modeling (Feature Specs). 5- Start meetings with Netcom engineer to create the request for new signals. 6. Review System Latency issue with ECG, phoenix domain controller, Netcom and Functional Arch team; engineer solutions as needed. |  |  |  |  |  |  |  | 
Root Cause: | Impacts 746/747. Feature Owners assigned 1/13/21. Feature development started late. Need 5D for UPV0. Find out no new ECU needed Phoenix Domain Controller will process signals /data. |  |  |  |  |  |  |  | 
Work Plan: | Steps |  |  |  |  | Target Completion Date |  | Target Completion Date | Lead
 | CDX746/7 Key Dates UPV0 ------------------------------------------------------------------------------------------------------------------------------------ UPV1 ------------------------------------------------------------------------------------------------------------------------------------ UPV2 ------------------------------------------------------------------------------------------------------------------------------------ FDJ --------------------------------------------------------------------------------------------------------------------------------------- DCV -------------------------------------------------------------------------------------------------------------------------------------- UPV0 1- Weekly meetings to address all containment issues (noted above) --------------------------------------------------- 2- Facilitate functional safety status ----------------------------------------------------------------------------------------------- 3- Facilitate cybersecurity ------------------------------------------------------------------------------------------------------------- 4- Provide FMA Status ----------------------------------------------------------------------------------------------------------------- 5- Design Data Analytics -------------------------------------------------------------------------------------------------------------- 6- Request Signals for DCV and Ethernet ----------------------------------------------------------------------------------------- 7- Feature Specs Complete ----------------------------------------------------------------------------------------------------------- 8- Freeze and Cascade Interface Requirements --------------------------------------------------------------------------------- UPV1 1- Create safety V&V report --------------------------------------------------------------------------------------- 2- Create cybersecurity V&V report------------------------------------------------------------------------------ 3- Evolve FMA & communicate status --------------------------------------------------------------------------------------------- |  |  |  |  | 1/27/20 5/22/20 8/26/20 12/11/20 2/17/20 3/26/21 9/27/21 1/27/22 2/18/22 4/11/22 8/22/22 11/27/22 |  | 03/11/21 06/11/21 08/24/21 12/03/21 04/04/22 Ongoing 06/16/21 04/14/21 05/23/21 05/03/21 04/23/21 04/16/21 05/31/21 06/07/21 06/07/21 06/07/21 | R. Li/Team R. Li/FuSa Team R. Li R. Li/FMA Coach R. Li R. Li/Netcom Eng B. Atherton B. Atherton R. Li/FuSa Team R. Li R. Li/FMA Coach
Risk Projections: | UPV0 | UPV1 | UPV2 |  | FDJ |  | Reference #: Date Issued: Date Revised: Date Closed: |  | 
 | Major | Minor | Contained |  | Contained |  |  |  | 
5D CDX746/7 Steering Horizon Controller UPV0
Notes: Open issues:
* systems application engineering and launch issues