## Slide 1
Steering Column/Pedal Position Control
(Manual Adjustment)
Turn Around
Automotive Operations
Modernize Everywhere
Disrupt Ourselves
VSEM Id: F004690
Programs: U71x MY25
Feature Owner: Barry Maloney
FuSa Engineer: Ashish Keshri

## Slide 2: Steering Column Position Control on U71X
Driver Seat Module
(DSM)
APIM_CDC
(Phoenix)
Column
Tilt Motor
HMI System (Steering Horizon Control)
Steering Column System
Column
Tele Motor
Switch Module
Display Module
The "Steering Column Position Control" allows the user to make adjustment to the Steering Column Position (Tilt/Telescopic) using capacitive switch on the steering wheel when ignition is in Accessory/On position (e.g., while vehicle is stationary/driving).
Safety Goal: Prevent impaired access to steering controls (ASIL B)
Rationale: Significant change in steering column position without user intent while vehicle is driving may result in impaired access to steering control.
SCCM, ECG
ASIL B
ASIL B
ECG
General flow for Column Pos Adjustment
Display Column Adjust
Hide Digital Switch
Idle Timeout
Touch?
1
4
Display Default Control
2
Display Driver
Adjust Control
3
Phoenix controls digital menu, contextual control and timeout
StewPosAdjTlt_D_Rq
StewPosAdjTel_D_Rq
Pos
Motor Signal
Motor Signal
Pos Info
Pos Info
Graphics info

## Slide 3: Pedal Position Control on U71X
Driver Seat Module
(DSM)
APIM_CDC
(Phoenix)
Pedal Motor
HMI System (Steering Horizon Control)
Pedal Position System
Switch Module
Display Module
The “Pedal Position Control" allows the user to make adjustment to the Pedal Position (Telescopic) using capacitive switch on the steering wheel when ignition is in Accessory/On position (e.g., while vehicle is stationary/driving).
Safety Goal: Prevent impaired access to pedal controls (ASIL B)
Rationale: Significant change in pedal position without user intent while vehicle is driving may result in impaired access to pedal control.
SCCM, ECG
ASIL B
ASIL B
ECG
General flow for Pedal Pos Adjustment
Display Pedal Adjust
Hide Digital Switch
Idle Timeout
Touch?
1
4
Display Default Control
2
Display Driver
Adjust Control
3
Phoenix controls digital menu, contextual control state and timeout
PdlAdj_D_Rq