## Slide 1
Ideation
Wallbox Vehicle Communication
This feature is a key enabler for other feature like: Power charge door, auto-authentication, Wallbox embracement, Charge status sync, Wallbox OTA via vehicle.
A fundamental feature to build up effortless, seamless, and premium private charging experience for customer. It will also bring value for Ford charging operation and aftersales diagnosis.
Nio all series, Tesla all series, Zeekr 001.
CX821, CX771, CX748
√
√
√
√
√
2024
√
√
-
√
Must to have enabled feature: auto-authentication, power charge door, Wallbox embracement, Charge status sync. Nice to have enabled feature: Wallbox OTA.
CX821
Strengthen information communication, Smoother home charging experience
User driving towards his parking lot. Smart Wallbox lights up （and projects the Lincoln Star） in the parking lot to Welcome Albert.
After plugging in, Wallbox and vehicle light changes. Albert knows charging will be started soon.
Albert pushes the button on the charging coupler and pull it out. Wallbox light changes and Vehicle charging door opens also with lighting. Vehicle also light up and shows current SOC level via exterior lighting. Albert plugs the coupler into vehicle naturally.

## Slide 2
BRD – Product Category
Product Name
Product Team: Charging Products
Product Owner: Jiayu Zeng
Date: 05-30-2022

## Slide 3: Content
Project Background
Business Purpose
Market/Competitive Analysis
Product Description
Sustainability Analysis
High-level Feasibility/Viability Check
Operations Needs & Impact
Risk Evaluation
Next Steps – Core Team

## Slide 4: Project Background
New feature. Major customers in China living in multiple dwelling with their parking lot in open area. Therefore, their Wallbox (come with BEV for free) will be installed in open area exposing to all residents with branding image.
When customer parking its vehicle, Wallbox will wake up and welcome customer with lighting. Customer pull out the charge coupler/naturally press the S3 button on the coupler. The charge port door on the vehicle automatically opens. Customer plug the couple into the vehicle. Wallbox is unlocked and the charging automatically starts. Wallbox can potentially remind customer via lighting if SOC is too low.
Many parking lots underground or in remote location may have limited cellular signal for Wallbox. Vehicle can download Wallbox OTA package and transmit the package via this communication. (already realized by Tesla)
This feature can also provide more diagnosis information and charging data via Wallbox and vehicle synchronization. By doing this, charging features like Preferred Charge Time can be enhanced. And customer charging issue diagnosis can be much more efficient.
Leading Programs
CX821, CX771, CX748
Timeline
—— Dev Start: TBD
—— E2E Test: TBD
—— Release: CX821 J1

## Slide 5: Business Purpose
Product Positioning（突出这次的优化项）
  从无到有建立一个cross car line 的基础性充电功能
Business Target
  有效实现车桩双向的近场可靠通信
  通信内容可以使能多种充电功能场景及功能需求
Corporate Value
  优化充电售后问题解决的数据基础

## Slide 6: Market Analysis - Industry Trend
This is to describe the industry trend, to analyze and predict where the market is moving.
Trend 1
  Major customer in China park their cars in open area of community. Excellent Wallbox can benefit Brand Promotion
Trend 2
  Effortless and premium charging experience will be the next levels of worry-free charging.
…

## Slide 7: Market Analysis - Customer Insight
Customer want effortless charging experience
  Plug in and charge. Fast and easy.
  Synced charging status provide better HMI.
Customer tend to show off premium experience feature
  Good opportunity in open parking area
Customer want a worry free aftersales charging solution
  Sync data can support better aftersales diagnosis capability

## Slide 8: Market Analysis - Competitor Intelligence
 | CX727 | Tesla Model Y | Nio EC6 | Zeekr 001
Charge Port Door |  |  |  | 
Motorized Door via Wallbox |  | Y | Y | Y
Auto-authentication |  | Y | Y | Y
Wallbox OTA via Vehicle |  | Y |  | 

## Slide 9: Product Description
How it works
1st Setup & Maintenance
CX727 As-Is:
Expect to Be:
First time charge at
Targeted places
(15mins or 1% SOC)
System record GPS/location
IVI Setting only:
1.Select history charging location
2. Set time period
3. Set Charging limitation specific for this feature
Arrived home and plug-in wallbox.
Make sure wallbox to be actived
Vehicle identify if target places or not.
If GPS identification is failed, then preferred charge time cannot be active.
Actual charging time calculation base on Target SOC. Do not meet customer expectation and cause confusion.
Charging at calculated time period which maybe earlier than ‘preferred time”
All Ford and Lincoln BEV users can easily Set preferred charging time per IVI or APP:
Set time period
Leverage universal charging limitation
Arrived home and plug-in wallbox.
Strictly charging at preferred economical charging time.
‘Charge Now’
Skip preferred time for 1 time if need to charge right away, but do not change overall regular plan.
7 Steps
3 Steps
Less complexity
More reliability

## Slide 10: Product Description- Wallbox-Vehicle Comm Focus
Albert gets off work and drives his Lincoln car back home
Albert driving towards his parking lot. Smart Wallbox lights up （and projects the Lincoln Star） in the parking lot to Welcome Albert.
Driving back home
On the road/
Preferred Charge Time
Lincoln knows today is the day for charging. Lincoln ask for Albert’s confirmation if he needs to charge vehicle at home tonight from XX PM to YY AM .
If Albert confirmed, Preferred Charge Time will be automatically set.
Parking with welcoming
Remind to charge /
Auto-authentication ready
After Albert getting off the vehicle, Wallbox light changes (and speak up). Albert knows his vehicle and Wallbox has finished the handshake. .
Wallbox and vehicle unlocked for charging
Albert pushes the button on the charging coupler and pull it out. Wallbox light changes and Vehicle charging door opens also with lighting. Vehicle also light up and shows current SOC level via exterior lighting. Albert plugs the coupler into vehicle naturally.
Albert knows he can focus on what to do tonight at home. Forget about the charging and leave.
Go home with no worry
After plugging in, Wallbox and vehicle light changes. Albert knows charging will be started soon.
Charging enabled

## Slide 11: Product Description-Some Potentials
Effortless Charging - Power Charging Door
Auto-authentication
Wallbox Embracement
- Light up for welcoming
Wallbox
Binded Vehicle
User driving approach parking lot and park vehicle.
Wallbox Embracement
- Illumination assist parking at darkness
Wallbox
Binded Vehicle
User get off vehicle.
Wallbox Embracement
- Vehicle SOC indication
Wallbox
Binded Vehicle
User operate Wallbox.
Vehicle Embracement- Charging light
Vehicle Charging Error Log
And other potentials…
Prefer charging time Embracement
- Vehicle setting and start charging time
Charge log Embracement
- Vehicle charging time
Charge level setting Embracement
Wallbox OTA through Vehicle

## Slide 12: Product Description-Use Cases
1
2
3
手机APP绑定激活车辆
并绑定家充桩开始设置车桩通讯
4
校验
车桩密钥
设置车桩通讯
车桩通讯的选配使用1-灯光互动
车桩通讯的选配使用2-充电盖板打开
车桩通讯的选配使用4-信息互动
5
车桩通讯的选配使用3-充电鉴权
车辆驶入停车场与桩端连接蓝牙
家充桩提示欢迎灯光
车辆停入车位打开车门
家充桩根据SOC 提示充电灯光
车桩蓝牙连接中车辆充电相关故障
家充桩提示车辆故障无法充电灯光
车辆存在预约充电
家充桩提示车辆等待充电灯光
车辆完成充电
家充桩提示车辆充电完成灯光结合SOC
按家充桩枪头按钮
车辆充电口盖板打开/关闭
插入充电枪至充电口
桩立即开启充电或进入等待充电
车辆故障信息
车辆插枪状态
车辆预约充电设置
车辆实际充电信息（开始结束时间，度数，时长）
车辆SOC
整个车桩通讯打开成功每个单独功能可以关闭/打开管理
家充桩无灯光互动
家充桩枪头按钮按无充电盖板打开
家充桩无车桩鉴权需刷卡或APP点击充电
家充桩无车桩信息的互动，桩端仅显示桩本身的信息数据
关闭整个
车桩通讯
选择不设置
校验通过
校验不通过
开启至少
一个功能板块
校验通过
识别车辆
SOC
Plan B: 欢迎灯光即识别SOC 提示不同灯效
插枪到拔枪
过程中识别
车辆故障
选择设置
打开上述功能体验需要进行新的一轮车桩通讯校验和设置
迎宾灯
车辆识别到插枪/拔枪成功
家充桩提示车辆插枪/拔枪灯光
使用灯
完成灯
识别车辆
SOC
识别车辆
充电状态
识别车辆
充电设置
识别车辆
插拔枪状态
家充桩状态和故障信息
车桩鉴权的交互信息
车桩通讯设置和使用中信息
其他充电相关信息
家充桩给车
车给家充桩

## Slide 13: Product Description-Feature List
大场景 | 分场景 | 优先级 | 触点 | 备注
设置和管理车桩通讯 | 家充桩通讯密钥的管理 | M |  | 
 | 车辆通讯密钥的管理 | M |  | 
 | 车桩通讯的开通*APP | H |  | 
 | 车桩通讯总开关和子功能开关的管理*APP | H |  | 
基于车桩通讯的灯光互动 | 迎宾灯效-车桩蓝牙已连上 | H |  | 灯效由家充桩开发完成
 | 根据SOC提示充电灯效（电量范围高/中/低）提示开始充电和充电已完成 | L |  | 
 | 根据车辆插拔枪状态灯效 | L |  | 
 | 根据车辆故障提示灯效 | L |  | 
 | 根据车辆设置预约充电提示灯效 | M |  | 
基于车桩通讯的充电盖板打开 | 充电枪按钮按下打开车辆充电口盖板 | H |  | 
基于车桩通讯的充电鉴权 | 车桩在插枪时完成鉴权开始充电 | H |  | 
基于车桩通讯的信息互动 | 车辆信息传递给家充桩(充电相关故障信息、插枪状态、SOC、预约充电设置、车辆实际充电情况等) *APP | H |  | 
 | 家充桩信息传递给车辆（状态和故障信息、车桩鉴权信息、车桩通讯信息）*IVI | M |  | 
其他基于车桩通讯的拓展功能 | 车辆充电上限同步家充桩 | L |  | 
 | 家充桩借助车辆信号OTA | L |  | 
MVP 实现

## Slide 14: Product Description -Solution concept
Wallbox
Motorized
Charging Port
Vehicle
EVSE
Charging
Sub-System
Power Transmission
Vehicle
Charging
Sub-System
Recognize user vehicle
Request seamless charging
Cellular
Module
IVI
Sync +
Provide Vehicle Identity
Respond seamless charging
Digital Cloud Connection
Wallbox
BT
Module
Additional
BT
Module
/ Existing BLEM
New Module
Existing Module
Legend
Bluetooth Connection
Other existing vehicle module

## Slide 15: Product Description -UX
我的家充桩主页
车桩通讯功能入口
车桩通讯开通须知
同意
返回
功能介绍
XXXX
个人信息告知
XXXXXX
前置条件提示：
已绑定车辆
已绑定家充桩
步骤1：车辆信息确认成功
步骤2：车辆信息密钥交换
信息校验
车桩通讯管理
开
车桩通讯总开关
开通成功！
3秒进入管理页面
车桩通讯
前置条件需要：
车辆已绑定且激活，家充桩已绑定
设置过程通过4G 云端/BLE 设置
若4G 需考虑桩端无信号如何处理
若BLE 需要考虑EVSS 云端校验密钥如何处理
关
开通后可以获得以下体验：
开
车桩鉴权
关
开
电动盖板
关
详情
开
信息互动
关
详情
开
灯光互动
关
迎宾灯
预约充电等待灯
故障灯
低电量需充电提示灯
灯光互动管理
更改
取消

## Slide 16: Sustainability Analysis

## Slide 17: High-level Feasibility/Viability Check
Wall Box Vehicle Communication
New BLE Module
Wall box cloud (3rd party)
Vehicle
Wall box
Charging Door
Complete Sync+ onboard process
Scan QR code to add wall box
Bind / Unbind Wall box with vehicle
Wall box BLE
Lincoln Way App
Request vehicle BLE and wall box meta data
Deliver vehicle BLE module Meta data
Get wall box data
BMS
[CAN message] Request to open charge door
[CAN message] Request to read SOC
Respond with wall box BLE and vehicle BLE meta data
EVSS
Wall Box SDK
Stores vehicle BLE meta data
Wall box info
Vehicle info
Get BLE key pairs linked to BUUID (from BLE module supplier)
BLE module private key written in supplier manufacturing plant.
BLE module provisioning
Stores wall box public key;
Vehicle related cloud
Get Vehicle data
Deliver wall box BLE meta data
Vehicle BLE private key
Wall box public key
Ford
New
Ford Existing Modify
3rd Party
New
Ford Existing No Change
3rd Party Existing No Change
3rd Party Existing Modify
Advertise with Beacon ID
Advertise with Wall box BUUID
Initiate BLE connection
Establish Secured BLE connection with wall box and vehicle BLE meta data
Within Power charging door Study Scope
ECG
Provisioning

## Slide 18: Operations Needs & Impact

## Slide 19: Risk Evaluation

## Slide 20: Next Steps – Core Team

## Slide 21
Thank You