## Slide 1: U554 ECDX IVI status
Expectation from Review:
Status update
Risk highlight

## Slide 2
  ECDX-U554 IVI E2E Validation Status – Issue Overview
Unsolved issues on R06.1 ENG2(Desay/Baidu)
Row Labels | Count of Key
Baidu | 14
Immediate Gating | 1
Gating | 13
Desay | 14
Immediate Gating | 4
Gating | 10
Grand Total | 28
Row Labels | Count of Key
Baidu | 38
Immediate Gating | 3
Gating | 35
Desay | 34
Immediate Gating | 5
Gating | 29
Grand Total | 72
44 issues already have fix plan in R06.1 PRO
Will retest 8/17 – 8/20
Unclose issues show as below:
Issue key | Summary | Component | Status | Fix version | Supplier | Risk | Occurrence | Recovery method
APIMCIS-15206 | MMOTA_China: SYNC+ upgrades status is not synchronous with ECG after installation if Sync+ reboot （example: when battery recovering from low charge) | MMOTA | Open |  | Desay | Middle |  | Master Reset
APIMCIS-15352 | Phase-4[U554]: No response to the startup password | PAAK | Open |  | Desay | High | 100% | N/A
APIMCIS-8601 | Phase-4[U554]: IVI screen cannot be woken up by stepping on the brake in LPR mode | PAAK | Open |  | Desay | High | 100% | N/A
APIMCIS-15354 | Phase-4[U554]: The IVI cannot be Light | PAAK | Open |  | Desay | High | 100% | N/A
APIMCIS-5472 | PM2.5 smart start function does not work | AAR | Open |  | Baidu | Middle | 100% | Hard reset
APIMCIS-15221 | V2I界面一直显示初始化，com.ford.xiaoduos.v2x进程没起来 | V2I | Open |  | Ford_Inhouse | Middle | 100% | N/A
Desay need to provide 5D report for U554 PAAK BSP failure
V2I crash happened R06.1 PRO(8/13), but no high light to Ford, which cause issue kept in R06.1 HF
R06.1 PRO HF new and regression issues
PAAK BSP function block
V2I function block
AAR smart start function failure

## Slide 3
  ECDX-U554 IVI E2E Validation Status – Have fix version IG Issue Overview
Issue key | Summary | Component | Supplier | Fix version | Occurrence | Risk | Recovery method
APIMCIS-14229 | MMOTA_China:After the Sync+ wifi connection, OTA upgrade failed through 4G and ECG reported "ERROR Curl7 | MMOTA | Desay |  |  | Middle | Master rest
APIMCIS-5274 | Phase4:CEN car to phone ,the phone unable to receive the push message | Connected Embedded Navigation | Baidu | R06.1 PRO | 100% | Low | N/A
APIMCIS-5470 | Phase4:[U554]It will be flash back when click message. | Message Center& Notification Pushing | Baidu | R06.1 PRO HF | 100% | High | N/A
Retest OK on R06.1 ENG2, regression and cause R06.1 to have HF version