## Slide 1: Performance Evaluation Result-S650-R06HF
Conclusion
Key Targets | Risk Assessment | Status | Evaluators
Response Speed | NA | Pass | Ford: Zhichao Zhang, Leo Jiang Baidu： Bing Chen, Qi Qian Desay：Wen Jie, Yafang Chen
Available Resource | NA | Pass | 
System Stability | Low | Pass | 
Open Jira | NA | Pass | 
Merged Performance Optimizations:
NA

## Slide 2: Performance Score & Bootup KPIs-S650-R06HF
Detail information
Performance Scores
Chart: 
| R04 | R05 | R006
Score | 73 | 83 | 83
Target | 84 | 84 | 84
No | Key Test Items | Target/s | Range of Gap | R06.HF2 Test result/s | Status
1 | Power on到Fast RVC显示 | 8 | 9 | 7.1 | 
2 | Power on第一帧动画播放 | 7 | 8 | 7.5 | 
3 | Power on Launcher界面可见 | 20 | 21 | 22.9 | 
4 | 用户开车门到Fast RVC显示 | 2 |  | 1.1 | 
5 | 用户开车门到第一帧动画播放 | 1 |  | 1.5 | 
6 | 用户开车门到launcher界面可见 | 14 |  | 16.9 | 
7 | Launcher显示到QQ音乐首次启动 | 4 | 4.6 | 1.1 | 
8 | Launcher显示到导航启动时间 | 13 | 13.65 | 13.8 | 
9 | Launcher显示到导航界面点击输入框下拉框 | 1.2 | 1.44 | 1.6 | 
10 | Launcher显示到语音可用 | 16.5 | 17.325 | 11.1 | 
11 | Launcher显示到语音播放音乐 | 5 | 5.75 | 3.2 | 
12 | Launcher显示到优先设备BT音源恢复 | 8 | 9 | 7 | 
13 | Launcher显示到QQ音乐恢复 | 4 | 4.6 | 5.7 | 
14 | Launcher显示到账号自动登录 | 1.5 | 1.8 | 2.3 | 
15 | Launcher显示到空调设置界面打开 | 2 | 2.4 | 1.6 | 
16 | Launcher显示到语音导航 | 3 | 3.45 | 2.6 | 
17 | 系统稳定状态下导航首次启动 | 3.3 | 3.795 | 5.9 | 
18 | 系统稳定状态下导航界面点击输入框下拉框 | 0.8 | 1.04 | 0.9 | 
19 | 系统稳定状态下，语音导航搜索时间 | 3 | 3.45 | 3.4 | 
Optimization Plan:
No.3,6: Launcher view layer is too deep to create in time, will re-develop on R07
No.8,9: Tiny gap
No.13: Network related.
No.14: No Updates.(Baidu)-AW2-22234
No.17: No Updates.(Baidu)-AW2-22226

## Slide 3: CPU/RAM/GPU/ROM Status-S650-R06HF
Detail information
Key | Key Parameter | Target | R06 | Status
1 | Reserved 1.6G buffer ROM Size on System & Vendor partition | 1.6G | Xxx(Desay) | Pass
Controller | Background | CPU Free (Target：>60%) | Status | GPU Free (Target: >40%) | Status | RAM Free (Target: >30%) | Status
开机3分钟，设置界面 | NA | 119% | Pass | 96% | Pass | 62% | Pass
前台导航中 | 唤醒语音+后台qq音乐播放（1min/次，关注语音音乐是否流畅卡顿） | 25% | Pass with condition | 45% | Pass | 54% | Pass
前台导航中 | 唤醒语音+后台BT音乐播放（1min/次，关注语音是否流畅卡顿） | 20% | Pass with condition | 46% | Pass | 52% | Pass
前台爱奇艺 | 唤醒语音+后台导航中（1min/次） | 80% | Pass | 87% | Pass | 50% | Pass
切换主题20次 | 后台导航中+qq音乐播放 | 86% | Pass | 94% | Pass | 42% | Pass
所有应用启动一次 | 后台导航中 | 137% | Pass | 87% | Pass | 51% | Pass
CPU loading Issue Assessment:
Xxx(Baidu)-AW2-22237