## Slide 1: ECG Flashing
If you have received a new bench and the ECG does not have a ribbon cable, you might need to install one.
    Orientation of the ribbon cable does not matter. But, ensure that the same orientation is used at both ends(ECG and Debug Board)
    The black connectors to secure the ribbon cables are extremely fragile.
    Try to leave the ribbon cable permanently installed.
    If the black connector breaks on the debug board, do not continue to use it as the ECG may display unreliable behavior.
To put it in fastboot, install the jumper on the 3rd pin(CCPU_UPDATE_N) from the sim card tray, and reboot the ECG. The ECG does not go to fastboot mode until rebooted.

## Slide 2: ECG Flashing (contd.)
Once you confirm that ECG is in fastboot mode (using Device Manager), open command prompt from within the out folder of the ECG SW folder.
Use the command “loadProduct.bat –b –r –s –gasd” for P702 gas
Use the command “loadProduct.bat –b –r –s –hev” for P702 hev
Use the command “loadProduct.bat –b –r –s –cx727” for CX727
Failure to use –r while flashing will limit the ECG from connecting to the VSDN and the modules will be stuck in “Unprovisioned” mode.
If flashing of VMCU for ECG fails, then put the jumper on USB_S pin (7th pin from sim card tray), reboot the ECG and run the command “loadProduct.bat –v –r –s –gasd/-hev/-cx727”. This will flash the VMCU alone.
Once you’re done flashing, please take the ECG out of fastboot mode for normal operation(remove jumper and reboot). If the ECG is still in fastboot, you wouldn’t be able to change DIDs on it.

## Slide 3: TCU Flashing
In order to flash the TCU, we need to put it in fastboot mode too.
There are 2 methods to do this –
    1. The same as ECG. Jumper on 3rd pin and reboot.
    2. Navigate to the “platform-tools” folder on your computer(provided with the drivers) and open command prompt from there. Send command “adb reboot bootloader”. You don’t have to reboot the TCU after this. Highly recommend method 1.
Once you confirm that the TCU is in fastboot mode, open command prompt from the “out” folder within the TCU SW.
Send command “loadProduct.bat” for flashing the SW. – The flags for this SW change now and then. Please confirm with release notes of that SW before flashing.
Once you’re done flashing, please take the TCU out of fastboot mode for normal operation(remove jumper and reboot). If the TCU is still in fastboot, you wouldn’t be able to change DIDs on it.