## Slide 1
CD764 Mini ICP Design Requirement
2). Mini ICP LIN to AUX for below buttons signal Transmit & Receive.
#2 HVAC Power---Touch button for HVAC on/off, AUX transfer LIN to Private CAN signal to IVI, w/ indicator from IVI.
#4 DAT Hot key---Touch button Hot key for TCS & Auto Hold , AUX transfer LIN to Private CAN send to IVI , w/o indicator.
#5 Temp Driver--- Hard button for Driver side temp adjusting +/-, w/o indicator from IVI.
#6 Blower Speed--- Hard button for blower speed adjusting +/-, w/o indicator from IVI.
#7 SDM---Hard button for SDM +/-, LIN transfer to Publish CAN signal to ABS, w/o indicator from ABS.
#8 A/C---Hard button for Compressor on/off, AUX transfer LIN to Private CAN send to IVI , w/ indicator from IVI.
#9 Temp Passenger--- Hard button for Passenger side temp adjusting +/-, w/o indicator from IVI.
1). Mini ICP Hardwire connected for below Buttons.
#1 Max Defrost, Touch button to RCCM and w/ indicator from RCCM feedback.
#3 Engine Start Stop, Touch button to RCCM and w/ indicator from RCCM feedback.
CD764 Post AA Console Surface
AUX
1
2
4
3
9
7
Mini ICP
Temp Driver
Blower Speed
A/C
Temp Pass
If continuous pressed #5 or #9 toggle up/down, IVI sent several events to RCCM
HMI pop up Driver Temp +/- change rate as 10 steps per 1 second, Control mirror time pop out is 2S.
Example: If continuous pressed Temp + , HMI change from 23.5C to 28.5C in 1 second, 0.5C per step
If continuous pressed #6 toggle up/down, IVI sent several events to RCCM
HMI pop up blower speed +/- change rate as 5 steps per 1 second, Control mirror time pop out is 2S.
Example: If continuous pressed Temp + , HMI change from 1 bar to 6 bar in 1 second
Blower Speed PoP out
SYNC+ Screen
Temp PoP out
SYNC+ Screen
5
6
8

## Slide 2
CD764 MFK Design Requirement
Function:
Hazard --- Hard wire connect to BCM, and w/o indicator from BCM feedback ；
Parking Menu --- Hard wire connect to ADAS/PAAM and w/o indicator from ADAS/PAAM ;
Vol +/-, Audio Power on/off--- LIN to AUX, AUX transfer LIN to Private CAN send to IVI , be pressed for audio power on/off, w/o indicator.
VOL
TEMP
1). MFK LIN to AUX , AUX transfer LIN to Private CAN.
CD764 Post AA Console MFK Design Assumption
MFK
AUX