## Slide 1: 22MY U55X Rear Seat Occupant Alert (RSOA) July 23rd. 2020

## Slide 2: Rear Seat Occupant Alert- RSOA
Background
  RSOA is new feature within Ford, to monitor vehicle conditions and remind the driver to check rear seat for occupants at ignition OFF.

## Slide 3: Proposed RSOA Feature Solution And Development Timeline- (Presented in CPRM 09-03-2019)

## Slide 4: Background MY20/MY21: RSOA Feature – How Does It Work?
Open/Close Rear Door
Ignition OFF ON
ARMED
Timer
Open/Close Rear Door
ARMED
Ignition OFF ON
Ignition ON OFF
Audible
Alert
“Chime”
Visual
Alert
Rear Seat Occupant Alert -- Variant 1

## Slide 5: Background MY20/MY21: RSOA Feature Description UX
Vehicle tile is on page 1 of settings for both 3.2v2 & SYNC 4
The rear seat pop-up will be displayed and audible tone will be heard for 10 seconds. A close button is also displayed to exit prior to 10 seconds notification.
8” and 10” Screen