## Slide 1
CD707 Mini ICP Design Requirement
Hazard
Vol Knob with power On/Off
Auto S/S
Max Defrost
Camera
Drive Modes
Parking
All ICE trims
Hazard
Vol Knob with power On/Off
Auto Hold
Max Defrost
Camera
Drive Modes
Parking
All FHEV trims
Mini ICP Hardwire connected for below Buttons
#1 Auto Start/Stop, Hardwire to RCCM and w/ indicator from RCCM feedback.
#2 Hazard, Hardwire to BCM w/o indicator.
#3 Parking menu, Hardwire to ADAS w/o indicator.
#4 Max Defrost, Hardwire to RCCM and w/ indicator from RCCM feedback.
Mini ICP LIN to IVI for below buttons
#1.1 Auto Hold Hot key---LIN to IVI , with indicator.
#5 Camera Hot key---LIN to IVI , w/o indicator.
#6 SDM Hot key---LIN to IVI , w/o indicator.
#7 Vol +/-, Audio Power on/off
LIN to IVI , Presse for audio power on/off, w/o indicator.
Short Pressed --- Audio on/off; Long Pressed --- Audio Restart.
Rotation for volume +/-
1
2
3
4
5
6
7
1.1