## Slide 1: Transport Layer Security
---EESE In-house FNV2 team
Sun Li & Liu Dapeng

## Slide 2: Content
Architecture
Introduction
TLS
IVI TLS

## Slide 3: Architecture

## Slide 4: Introduction
Why use TLS?
In order to curb the outside attack, ECG and its connected nodes must implement some security measures. TLS authentication is one of the implemented features.
What is TLS?
TLS is short for Transport Layer Security. It should be used to secure the TCP/IP network traffic over the in-vehicle Ethernet.
Who will use TLS?
ECG and other fast ECUs(such as SYNC, TCU or any other modules on Ethernet participating in the SOA communication with ECG).

## Slide 5: Introduction
Which components help ECG support TLS?
MQTT broker
  ACL configuration file
  ACL built in the Mosquitto broker is a basic implementation. ACL configuration is a simple text file which could be tricky to update.
  Mosquitto_auth plugin
  It supports a large number of databases especially more suitable for ACL management.

## Slide 6
Introduction
Which component will be responsible for TLS on IVI?
SOA gateway
  SOA gateway will establish a single TLS session on behalf of all the clients.
  Certificate
  key management
      TLS RSA key pair

## Slide 7: TLS
Version
  TLS v1.2
TLS Cipher suite selections
    TLS_ECDHE_RSA_WITH_AES_256_CBC_SHA384_P384
    TLS_ECDHE_RSA_WITH_AES_128_CBC_SHA256_P256
    TLS_ECDHE_RSA_WITH_AES_256_CBC_SHA_P384
    TLS_ECDHE_RSA_WITH_AES_128_CBC_SHA_P256

## Slide 8: TLS
TLS digital certificate
  X.509
    RSA-2048 key
    Sha256

## Slide 9: TLS
Key storage and management
SYNC
|-- RSA-2048 key pair
| |-- SYNC_SOA_Auth_RSA-2048_cert
| `-- SYNC_SOA_Auth_RSA-2048_priv_key
`-- ECG_SOA_CA_RSA-cert
ECG
|-- RSA-2048 key pair
| |-- ECG_SOA_Auth_RSA-2048_cert
| `-- ECG_SOA_Auth_RSA-2048_priv_key
|-- SYNC_SOA_CA_RSA-cert
`-- TCU_SOA_CA_RSA-cert
TCU
|-- RSA-2048 key pair
| |-- TCU_SOA_Auth_RSA-2048_cert
| `-- TCU_SOA_Auth_RSA-2048_priv_key
`-- ECG_SOA_CA_RSA-cert

## Slide 10: IVI TLS
RSA-2048 key pair
    SYNC_SOA_Auth_RSA-2048_cert
    SYNC_SOA_Auth_RSA-2048_priv_key
ECG_SOA_CA_RSA-cert
SOA Gateway contains secure TLS connection
    Headers contains all the paths to enable a secure TLS connection
        CERT_ECG_SOA_TLS_CA - ECG CA Certification location
        CERT_CLIENT_SOA_TLS_PUBLIC - client public TLS certificate location
        KEY_CLIENT_SOA_TLS_PRIVATE - client private TLS key location
    key-store library what we link to get paths so SOA Gateway can read certificates and keys

## Slide 11
Global & Local Security Team(Local contact: Huang Eric)
  Clarifying the requirement and corresponding specification;
  Providing keys and certifcaes
  Providing TLC component libraries
  Providing the correct TLS format for SYNC+;
REC & Desay Team
  Integrate keys and certificates which will be used in TLS session on DuerOS
  implement the APIs of write /read the certificates and keys.
FNA (SOA Gateway) Team
  Provide the APIs and Libraries of SOA gateway and make sure the SOA Gateway can access the certificates and keys on target.
Scope & Next Steps

## Slide 12
Thank you