## Slide 1: IVI Provisioning Analysis
LIU Chenxi / DSV NKG
Rev01 @ Feb 25,2020
Notes: Rev01 Feb 25,2020 LIU Chenxi initial verison

## Slide 2: System architecture
Feature Description:
IVI provisioning is to register unique information for each dedicated AHU in baidu cloud side.
This feature setup the fundamental base for further service authentication / charging / personalization and etc.

## Slide 3: Interaction Sequence
Feature Description:
Suggestions:
AHU connectivity management (WIR connection).
Security management for AHU and Baidu Cloud regarding to Ford specified service.
DuerOS UUID management.
Baidu cloud UUID management.
Use Case Examples:
Suggestions:
AHU ONLY power on internal WIFI post DE00 configured.
Each Ford AHU unit has a Ford specified “birth certificate” which is similar with Ford SupplierFeed metadata. Baidu cloud only provides UUID for AHU units with Ford specified “birth certificate” .
DuerOS issues “Marriage Request” to obtain new UUID if any of the vehicle info changes.
Baidu cloud updates UUID table for new “AHU-VIN marriage”.
Sketch/Picture:
Business Owner:
Feature Champion:
Feature Owner:
Workstream Source:
Feature Funding Source:
Proposed Implementation Timing: Appl. Ready?
MONETIZATION
In Vehicle / Out of Vehicle Experience? x In □ Out □ Both
Projected Monetization:
Revenue at Point of Sale (of vehicle/service)__________________
Subscription / Pay Per Use Model _________________________
B2B Model (e.g. from data sets) ___________________________
Other _______________________________________________
AHU
(
DuerOS
)
Baidu
Cloud
Provision
State
UUID Status
Check Provisioning Trigger
Pre
-
conditions
(
meet
)
Issue Provisioning Alert
(
VehInfo
+
AHU MetaData
)
Generate
UUID
Assign UUID
Factory Mode
VSCS Configured completed
Unprovisioned
Waiting for
Provisioning Ack
Provisioning
Success
Null
Assigning UUID
Provisioning Ack
Waiting for UUID
Provisioning
Started
Stored UUID
UUID Ack
Update UUID
–
Veh
matrix
DuerOS Provisioning Happy Path
Check
MetaData
Validity
WIR connection
(
DuerOS connects with cloud
)
Note
:
AUH follows Ford Power Mode Management in any of Provision State
.

## Slide 4: Assumption on current AHU
Feature Description:
This is the work package assumption for current AHU product
There is a dedicated application to control every detailed procedure for provisioning
All the components are from baidu

## Slide 5: Analysis for SYNC 4
Feature Description:
This is the work package analysis for the ongoing SYNC 4
Giving the condition that re-use existing system / assets as much as possible

## Slide 6: Analysis for SYNC 4 (cntd.)
Feature Description:
It’s estimated that badu provioning app will be kept.
Therefore the interaction between AHU and baidu clode is considered to be ready or almost ready with few adaption to DSV framework and service
In this case, DSV responsibility for provisioning is just providing necessary meta data requested

## Slide 7: Meta data
Feature Description:
Meta data required by baidu provision app (actually from badu cloud) is similar with the data set for peripheral provisioning ( ford cloud)
These are the meta data (which is called ProvOnBoardClient 3 (SYNC)
Ethernet channel is adopted in CVPP
R/O (*) | Name | Attribute | Datatype | Based64 encoded | Length | Sample
R | FESN | 0xF17F | ASCII | No | 8 chars | 1EG004Q6
R | SecurityKeyPackageID | 0xD03D | ASCII | Yes | 40 chars. | EF9FAD62EAD4DA9E635BAFCE8E6B7A50AD0D8B62
R | Hardware/CoreAssembly Part Number | 0xF111 | ASCII | No | 24 chars. | 
R | Software Part Number | 0xF188 | ASCII | No | 24 chars. | 
R | Calibration Config Part number | 0xF10A | ASCII | No | 24 chars. | 
R | Delivery Assembly Number | 0xF113 | ASCII | No | 24 chars. | 
R | part2Partnumber | 0xF110 | ASCII | No | 20 chars. | 
R | ECUID | ECU ID is an unique and fixed value for each ECU | Hexadecimal | Yes | 8 chars. | 
R | ECU_Provisioning State (ECUProvDID) | 0xD021 | Hexadecimal | Yes | Enum 24 chars. | 
O | Ethernet Mac Address | ECU internal data | ASCII | No | 17 chars. | 
O | Wi-Fi Mac Address | 0xFD26 | ASCII | No | 17 chars. | 
O | Bluetooth Mac Address | ECU internal data | ASCII | No | 24 chars. | 
O | Firmware Version | 0xFD12 and 0xFD15 | ASCII | No | 50 chars. | 
O | Primary Bootloader Part Number | CCPU: 0x8068 VMCU: 0xD027 | ASCII | No | 24 chars. | 
O | Recovery load part number | CCPU: 0xEEFF VMCU: 0xEEFE | ASCII | No | 24 chars. | 
O | Global Configuration Version | Refer to ECU part II spec | ASCII | No | 50 chars. | 

## Slide 8: References
Peripheral Module Provisioning SPSS v1.4.pdf
Draft EOL provisioning_v1.pptx
DuerOS AHU EOL Provisioning with Baidu Cloud - Phase 4 _v2.xlsx